## Slide 1: Investigate time series neural data: Experimental design & processing
Day 3 : LAB
Tutors: Mark Butler and Monika Sharma

## Slide 2: Experiment Description
TMSI Refa8 EEG amplifier
  Sampling rate: 256 Hz
  17 electrode: fronto-central, central, centro-parietal, and parietal
OpenVIBE software
  EEG recording
  display of visual cues
  Feedback
  Online classification

## Slide 3: EEG Concept
Concept | Details | Why Important
EEG Channels | Records change in voltage over time | Represents spatial brain activity
Number of Channels | Can vary: • Low-density: 8–16 channels • Medium: 16–32 channels • High-density: 64, 128, 256+ channels | More channels = better spatial resolution
10–20 System | Standard electrode placement system | Ensures consistency across studies
Odd vs Even Electrodes | Odd = Left hemisphere (C3, FC3, CP3) Even = Right hemisphere (C4, FC4, CP4) | Helps distinguish left vs right brain activity
Midline Electrodes | Cz, FCz, CPz (“z” = center) | Represent central brain activity
Sampling Frequency | Number of samples per second; your system: 256 Hz | Determines temporal resolution and ability to capture fast neural activity
EEG Frequency Bands | Alpha (8–13 Hz): relaxed, eyes closed; Beta (13–30 Hz): alert, active thinking | Alpha → baseline/relaxation; Beta → cognition, attention, stress

## Slide 4: Participants and tasks
Sixteen naive participants
  13 males and three females
  mean age = 28 ± 9 years
Tasks
  cued motor imagery (They imagined movement based on cues)
  left hand, right hand, left foot, and right foot
  Each session
    24 trials for each motor imagery task
Visual or somatosensory feedback

## Slide 5: Recorded EEG signal analysis
EEG signal were 5s epoched from 1s before feedback onset
Bandpass filtered [0.5, 40] Hz
re-referenced at Fz
common spatial patterns (CSPs) to extract the feature vectors
linear discriminant analysis (LDA) classifier
selecting a time window around an important event

## Slide 6: Exercises
Temporal filter: Apply a low-pass filter of your choice with a cut-off at
  6 Hz
  32 Hz
Spatial filter: Apply a Laplacian filter for electrodes
  FCz, Cz and CPz
Baseline correct the
  temporally filtered data
  spatially filtered data
Plot the grand averages of the electrodes: Cz, FCz and CPz for the time range [1.5, 3] s
Plot and analyse the time-frequency distribution of the signals using Morlet Wavelet
  temporally filtered data
  spatially filtered data